## Slide 2: Library QA & QC
Day 1, Video 3
  Experimental considerations for library construction
  Considerations for input material
  Quantification by Qubit
  Quality control by Bioanalyzer
  Quantification and quality control by qPCR

## Slide 3: Experimental considerations
Single read vs. Paired end reads
Read length
Sequencing Depth/Coverage
Replicates
These will direct you to a specific platform
  MiSeq: 15-25M clusters per run, 50-300bp read length
  HiSeq v3: 150-200M clusters per lane, 50-100bp read length
Coverage = bp Sequence
bp Genome

## Slide 4: Input – DNA (genomic DNA)
Which method or kit to use?
  How much: >1 ug or <10 ng
  What is the quality?
  How will you fragment?
  What is your optimal insert size, does it matter?
  Are you concerned about amplification bias (high/low GC, etc)
Other considerations:
  Multiplexing: how many do you need to get on one lane
  Is there a reference genome available?

## Slide 5: Input - RNA
Which method or kit to use?
  How much: >1 ug or <10 ng or single cell
  What is the quality?
  Total RNA vs. poly-A RNA vs. ribosomal removal
  Strand specific or not?
Unlike with DNA sequencing/resequencing these questions will often depend on what question you are asking
  Differential expression
  Isoform analysis
  De novo transcriptome assembly

## Slide 6: ChIP-Seq
Library kits available that deal with low input, but most of the steps are performed outside of a kit
Every step likely requires some optimization
  Antibody choice – require good signal to noise
  No antibody controls
  Crosslinking reagent and time
  Fragmentation

## Slide 7: Always check the quality of your input material!
gDNA:
  Intact, high MW DNA on agarose gel
  Quantify input by Qubit (fluorescent DNA and RNA assays)
  Check size after fragmentation on Bioanalzyer
Total RNA:
  Run on Bioanalyzer RNA nano or RNA pico
  Quantify RNA by Qubit (RNA assay)
  Check ribosomal removal before fragmentation
ChIP:
  check no-antibody controls
  Check size after fragmentation on Bioanalyzer

## Slide 8: Quantification of DNA/RNA
Use a fluorescent method – Qubit or picoGreen
  Dye binds specifically to dsDNA or RNA
  In many cases measure both DNA and RNA by Qubit
  Nanodrop quantification can be off by an order of magnitude!
Requires ~2uL sample

## Slide 9: Bioanalyzer – what’s the deal?
Agarose gel meets microfluidics - Measures fluorescence (DNA or RNA) versus time
  Great for size estimates at low concentrations
  Great for determining quality of total RNA
  Not so great for quantification

## Slide 10: Determination of input RNA quality
RNA Nano (5-500 ng/uL) or RNA Pico (50-5000 pg/uL)
RNA Integrity Number (RIN) indicator of quality
Monitor rRNA depletion

## Slide 11: During library construction
Check for problems:
  Over-amplification
  adapter-dimer, primer-dimer, excess primers
Determine size range of final library
Adapter-dimer
Excess
primers
Over-amplification
High Sensitivity DNA chip (5-500 pg/uL)
Monitor fragmentation (RNA or DNA)

## Slide 12: Final QC - qPCR
Primers for P5 and P7 ends of the adapters – only detect molecules with both adapters bound
Requires significant dilution, can lead to large errors
Final concentration calculation depends on the size of your library
Adapter-dimers WILL be amplified (can check on gel after qPCR)

## Slide 13: Comparison between methods
Rarely see the same concentration by Qubit, Bioanalyzer and qPCR
  Ratios between qPCR:Qubit (molar) typically between 0.8-2.0 for well-performing libraries
  Higher ratios may indicate over-amplification or significant adapter-dimer, check the Bioanalyzer
  Low ratios may indicate a problem with adapter ligation
It is better to make a new library than to sequence a terrible library!!

## Slide 14: QC and sequencing facilities
Every facility has their own proven method – trust the experts and have them do quantification even if you have already done it!
  Every instrument is slightly different
  Relationship between loading concentration and cluster density is not a simple one!
Everything about your library is important for your sequencing facility to know
    Library construction method, quality of input, size distribution, strain/species, potential low sequence complexity, barcoding method, previous performance (if known), etc.